## Slide 1
DRAM Individual Test
memtester
Memtest86+
3/15/2021

## Slide 2
memtester
1 | Stuck Address
2 | Random Value (32-bit wide Random)
3 | Compare XOR
4 | Compare SUB
5 | Compare MUL
6 | Compare DIV
7 | Compare OR
8 | Compare AND
9 | Sequential Increment
10 | Solid Bits
11 | Block Sequential
12 | CheckerBoard
13 | Bit Spread
14 | Bit Flip
15 | Walking Ones
16 | Walking Zeros
17 | 8-bit Writes (8-bit wide Random)
18 | 16-bit Writes (16-bit wide Random)

## Slide 3
1 - Stuck Address
0x1a000000
0xe5fffffB
0x1a000008
0xe5fffff3
Unsigned long * pUL
0x1a000000
0x1a000004
0x1a000008
0x1a00000c
交替寫入相對應 Address值及反向Address值

## Slide 4
2 - Random Value
0x3fd797b1
0xd9b8762a
0xc43df760
0x8ae724b8
Unsigned long * buf1
Unsigned long * buf2
0x3fd797b1
0xd9b8762a
0xc43df760
0x8ae724b8
32-bit wide Random

## Slide 5
3 - Compare XOR
0x3fd797b1^x
0xd9b8762a^x
0xc43df760^x
0x8ae724b8^x
Unsigned long * pUL
unsigned long x = random_ul();
將全部 data XOR 某一random值

## Slide 6
4 - Compare SUB
0x3fd797b1-x
0xd9b8762a-x
0xc43df760-x
0x8ae724b8-x
Unsigned long * pUL
unsigned long x = random_ul();
將全部 data SUB 某一random值

## Slide 7
5 - Compare MUL
0x3fd797b1*x
0xd9b8762a*x
0xc43df760*x
0x8ae724b8*x
Unsigned long * pUL
unsigned long x = random_ul();
將全部 data MUL 某一random值

## Slide 8
6 - Compare DIV
0x3fd797b1/x
0xd9b8762a/x
0xc43df760/x
0x8ae724b8/x
Unsigned long * pUL
unsigned long x = random_ul();
將全部 data DIV 某一random值

## Slide 9
7 - Compare OR
0x3fd797b1|x
0xd9b8762a|x
0xc43df760|x
0x8ae724b8|x
Unsigned long * pUL
unsigned long x = random_ul();
將全部 data OR 某一random值

## Slide 10
8 - Compare AND
0x3fd797b1&x
0xd9b8762a&x
0xc43df760&x
0x8ae724b8&x
Unsigned long * pUL
unsigned long x = random_ul();
將全部 data AND 某一random值

## Slide 11
9 - Sequential Increment
x
x+1
x+2
x+3
Unsigned long * pUL
unsigned long x = random_ul();
循序+1

## Slide 12
10 - Solid Bits
0xffffffff
0x00000000
0xffffffff
0x00000000
Unsigned long * pUL
取Pattern與反向pattern交替寫入

## Slide 13
11 - Block Sequential
0x00000000
0x01010101
0x02020202
0x03030303
Unsigned long * pUL
每個byte都Sequential Increment

## Slide 14
12 - CheckerBoard
0x55555555
0xaaaaaaaa
0x55555555
0xaaaaaaaa
Unsigned long * pUL
Solid Bits的特殊狀態，取容易出錯的Pattern檢測，通常是55AA

## Slide 15
13 - Walking Ones
0x00000001
0x00000002
0x00000004
0x00000008
Unsigned long * pUL
1向左shift循序寫入

## Slide 16
14 - Walking Zeros
0xfffffffe
0xfffffffd
0xfffffffb
0xfffffff7
Unsigned long * pUL
0向左shift循序寫入

## Slide 17
15 - Bit Spread
0x01010101
0x02020202
0x04040404
0x08080808
Unsigned long * pUL
每個byte都Walking Ones

## Slide 18
16 - Bit Flip
0x00000001
0xfffffffe
0x00000002
0xfffffffd
Unsigned long * pUL
0x00000004
0xfffffffb
0x00000008
0xfffffff7
Solid Bits+Walking Ones

## Slide 19
17 - 8-bit Writes
0x3f
0xd7
0x97
0xb1
Unsigned char * pUC
8-bit wide Random

## Slide 20
18 - 16-bit Writes
Unsigned char * pUC
0x3fd7
0xd9b8
0xc43d
0x8ae7
16-bit wide Random

## Slide 21
Memtest86+
1 | Address test, walking ones
2 | Address test, own address
3 | Moving inversions, ones&zeros
4 | Moving inversions, 8 bit pattern
5 | Moving inversions, random pattern
6 | Block move, 64 moves
7 | Moving inversions, 32 bit pattern
8 | Random number sequence
9 | Modulo 20, Random pattern
10 | Bit fade test, 2 patterns
11 | Hammer Test

## Slide 22
1 - Address test, walking ones
0x00000001
0x00000002
0x00000004
0x00000008
Unsigned long * pUL
0x1a000000
0x1a000004
0x1a000008
0x1a00000c
1向左shift循序寫入

## Slide 23
2 - Address test, own address
0x1a000000
0x1a000004
0x1a000008
0x1a00000c
Unsigned long * pUL
0x1a000000
0x1a000004
0x1a000008
0x1a00000c
寫入相對應 Address值

## Slide 24
3 - Moving inversions, ones&zeros
0xffffffff
0xffffffff
0xffffffff
0xffffffff
Unsigned long * pUL
check
0x00000000
0xffffffff
0xffffffff
0xffffffff
check
0x00000000
0x00000000
0xffffffff
0xffffffff
check
0x00000000
0x00000000
0x00000000
0xffffffff
check
0x00000000
0x00000000
0x00000000
0x00000000
Forward

## Slide 25
3 - Moving inversions, ones&zeros
0xffffffff
0xffffffff
0xffffffff
0xffffffff
Unsigned long * pUL
check
0x00000000
0xffffffff
0xffffffff
0xffffffff
check
0x00000000
0x00000000
0xffffffff
0xffffffff
check
0x00000000
0x00000000
0x00000000
0xffffffff
check
0x00000000
0x00000000
0x00000000
0x00000000
Backward

## Slide 26
4 - Moving inversions, 8 bit pattern
0x01
0x02
0x04
0x08
Unsigned char * pUC
check
0xfe
0x02
0x04
0x08
check
0xfe
0xfd
0x04
0x08
check
0xfe
0xfd
0xfb
0x08
check
0xfe
0xfd
0xfb
0xf7
8 bit moving inversions with walking ones pattern

## Slide 27
5 - Moving inversions, random pattern
0xac
0x48
0xb6
0x3d
Unsigned char * pUC
check
0x53
0x48
0xb6
0x3d
check
0x53
0xb7
0xb6
0x3d
check
0x53
0xb7
0x49
0x3d
check
0x53
0xb7
0x49
0xc2
8 bit moving inversions with random pattern

## Slide 28
6 - Block move, 64 moves
0x0101010101010101
0x0202020202020202
Unsigned long long * pULL
check
0x0404040404040404
0x0808080808080808
0xfefefefefefefefe
0x0202020202020202
check
0x0404040404040404
0x0808080808080808
0xfefefefefefefefe
0xfdfdfdfdfdfdfdfd
check
0x0404040404040404
0x0808080808080808
0xfefefefefefefefe
0xfdfdfdfdfdfdfdfd
check
0xfbfbfbfbfbfbfbfb
0x0808080808080808
0xfefefefefefefefe
0xfdfdfdfdfdfdfdfd
0xfbfbfbfbfbfbfbfb
0xf7f7f7f7f7f7f7f7

## Slide 29
7 - Moving inversions, 32 bit pattern
0x00000001
0x00000002
0x00000004
0x00000008
Unsigned long * pUL
check
0xfffffffe
0x00000002
0x00000004
0x00000008
check
0xfffffffe
0xfffffffd
0x00000004
0x00000008
check
0xfffffffe
0xfffffffd
0xfffffffb
0x00000008
check
0xfffffffe
0xfffffffd
0xfffffffb
0xfffffff7

## Slide 30
8 - Random number sequence
0x3fd797b1
0xd9b8762a
0xc43df760
0x8ae724b8
Unsigned long * buf1
Unsigned long * buf2
0x3fd797b1
0xd9b8762a
0xc43df760
0x8ae724b8
0x3fd797b1
0x264789d5
0x3bc2089f
0x7518db47
Unsigned long * buf1
Unsigned long * buf2
complement
0x3fd797b1
0x264789d5
0x3bc2089f
0x7518db47

## Slide 31
9 - Modulo 20, Random pattern
Using the Modulo-X algorithm should uncover errors that are not detected by moving inversions due to cache and buffering interference with the algorithm.A 32 bit random pattern is used.

## Slide 32
10 - Bit fade test, 2 patterns
The bit fade test initializes all of memory with a pattern and then sleeps for a few minutes. Then memory is examined to see if any memory bits have changed. All ones and all zero patterns are used.

## Slide 33
11 - Hammer Test
Repeatedly accessing addresses in the same memory bank but different rows in a short period of time.