## Slide 1: TCG Opal Storage Architecture Core Overview
Eng. III SW
Jai

## Slide 2: Reference
[1] Trusted Computing Group (TCG), “TCG Storage Architecture Core Specification”, Version 2.01
[2] Trusted Computing Group (TCG), “TCG Storage Security Subsystem Class: Opal”, Version 2.01
[3] Trusted Computing Group (TCG), “TCG Storage Opal SSC Test Cases Specification”, Version 2.01
[4] Trusted Computing Group (TCG), “TCG Storage IEEE1667 Opal Test Cases Specification”, Version 1.00
*Trusted Computing Group (TCG), “TCG Storage Security Subsystem Class: Enterprise”, Version 1.00
*Trusted Computing Group (TCG), “TCG Storage Security Subsystem Class: Opalite”, Version 1.00
*Trusted Computing Group (TCG), “TCG Storage Security Subsystem Class: Pyrite”, Version 1.00
SSC
Opal, Enterprise, Opalite & Pyrite
General
Specific
Test Cases
Compliance & Test Cases
TCG Storage Architecture Core Specification
Storage Interface

## Slide 3: Agenda
Section 1
  Trusted Storage Device Introduce
  Security Providers
  Take Ownership Model
Section 2
  Tables & Methods
  Templates
  Access Control
  Communication
Section 3 …

## Slide 4: Section 1 Abstract

## Slide 5: Why Security ?
Host Interface
Loadable FW
Function
Logical Storage
Special HW Func.
System Block
Easy to crack
Readable
Protect the confidentiality of stored user data against unauthorized access once it leaves the owner’s control
Strong Access Control
Unobservable cryptographic operation of secret for more faster, for more secure

## Slide 6: TCG Spirit and Prevention
Host Application
Trusted Storage
Trusted Commands
Interface
ATA / SCSI
Cryptography Firmware & Hardware
T10 (SCSI) / T13 (ATA)
Security Provider
Hidden Storage
Assign Hidden Storage to app by ISV

## Slide 7: Trusted Storage Device Architecture Overview
Multicomponent Trusted Platform
supports 1 or more TPers
Trusted Peripheral
Security Provider
Tables & Table Content
Methods
Authorities
Access Control List &
Access Control Elements
bilateral enrollment & connection
Data confidentiality and access control over TPer features and capabilities
Readable and writeable data areas
Built-in firmware/Hardware functions
SPs support functions such as
Authentication
Secured attribute-value storage
Disk encryption/decryption
Backup
Time stamping
Event logging

## Slide 8: Trusted Storage Device Architecture Overview

## Slide 9: Security Providers (SPs)
SP
Authorities
User 1
User 2
…
SP Method
ACL = user 1
Table
Method Name | ACL
Function 1 | User 4
Function 2 | User 1
Set | User 1
Get | User 2
A Security Provider is a set of tables and
methods that control the persistent trust state of the SP and MAY participate in control of the persistent
trust state of the TPer.
SPs are created by manufacturer & OEM
AND/OR Issuance
SPs have its
own storage, functional scope, and security domain
Tables. The two types of tables are described in Section 3.2.5. Tables consist of rows and columns.
Table content is the persistent state information of the SP.
Methods. Method operations include functions such as: table additions, table deletion, table read access, and table backup.
Authorities specify passwords or cryptographic proofs required to become authenticated within a session to the SP.
Access Control Lists (ACLs) and Access

## Slide 10: Ownership Overview
Manufacturer to define TCG functions are performed
Who has access to these functions
How the TPer and SPs communicate with the Host
When these events are permitted and when the events are logged.
SPs are created by the manufacturer during Storage Device creation, or through the Issuance process

## Slide 11: Host <--> TPer Communication Infrastructure
The only way to communicate with an SP is via a session.
Only the host is able to open a session.
Methods are invoked within sessions.
Host
Trusted Command
(i.e. T10 SECURITY PROTOCOL IN/OUT
or T13 TRUSTED SEND/RECEIVE)

## Slide 12: MSID Credential
The MSID Credential value is set at manufacturing time by the storage device vendor and is typically printed on the storage device label. It represents the device's initial storage device SID Credential value (owner's password) and uses that value to authenticate to the SID authority in the Admin SP, and then change the SID from its default value.
The MSID Credential is a PIN credential that does not have an associated authority. Rather, the MSID is used to store a fixed PIN value that can be read over the interface by the host by anybody.

## Slide 13: MSID Credential
Opal, Opalite and Pyrite SSCs borrow the concept of MSID from the Enterprise
Opal SSC 2.00 and subsequent versions introduced an additional option, to set the default SID credential to a Vendor Unique value other than MSID.

## Slide 14: MSID Credential
MFG manufactured an SED (Self-Encrypting Drives)
Shipped to a PC/Notebook OEM.
The OEM integrates the SED into the PC/Notebook but does not execute any procedure to take ownership.
The OEM includes trial security software for managing the SED, into which the user can opt.
A user purchases this PC/Notebook and does not opt into the security software offering. The user may not be aware of, or may not care about, the security features offered. This user will use the PC/Notebook as if it contained a non-SED.
In this scenario, since neither the OEM nor the end user took steps to take ownership by changing the SID PIN, the value of the SID PIN will still be the same as the MSID Credential value and what is readable by anybody.

## Slide 15: Section 2 Specification

## Slide 16: Security Providers
SPs are created by manufacturer & OEM AND/OR Issuance
SPs have its own storage, functional scope, and security domain
A SPs is a set of tables and methods that control the persistent trust state of the SP and MAY participate in control of the persistent trust state of the TPer.

## Slide 17: Table
Tables SHALL be stored in SP-specific parts of the secure storage area of the TPer. The SP-related secure storage area(s) of a TPer SHALL only be accessible via the host interface-specific IF-SEND and IF-RECV commands

## Slide 18: Table
There are two kinds of tables : Byte Table & Object Table
Byte Table | 
Index | Column
0 | 0x00
1 | 0x30
2 | 0x40
… | 
n | 0x41
The address of the first row in a byte table is 0
Upon creation, the value of all cells in a byte table SHALL be 0x00, length is one byte
Object Table |  |  | 
UID | Column 1 | Column 2 | Column 3
8 byte UID 1 | Data | Data | Data
8 byte UID 2 | Data | Data | Data
… | … | … | …
The columns of the object table define the contents of each object in it. And have same type
Object tables provide storage for data that binds a set of methods and access controls to that data.
This column contains an 8-byte unique identifier for that row. Each row has an SP-wide unique value in this column

## Slide 19: Method
Methods are remote procedure calls invoked by the host to manipulate SP state, methods operate on table or SP itself, and are used for session startup, authentication, table manipulation and access control customization.
Table Management
Table read/write
Authentication
Access Ctrl. Management

## Slide 20: Method
A method invocation is made up of the following parts:
Header
  InvokingID
  MethodID
Parameter
  Required parameters
  Optional parameters
InvokingID.MethodID [parameters] ==> Method Result
This is the 8-byte UID of the table, object, or SP upon which the method is being invoked.
This is the 8-byte UID of the method being invoked
This is a list of the parameters submitted to the method. These parameters MAY be one of two types.
Send by Host
Generated & Response from TPer

## Slide 21: Method

## Slide 22: Template
Base Template: Provides the tables and methods common for all SPs.
Admin Template: Provides administrative control over other SPs and the TPer settings as a whole, and control over Issuance of new SPs.
Clock Template: Contains tables and methods specialized for forensic and cryptographic clocks.
Crypto Template: Contains functional extensions to the Base SP cryptographic and procedural capabilities.
Locking Template: Provides tables and methods for storage encryption/decryption and read/write lock state control.
Log Template: Contains tables and methods specialized to forensic logging.
Templates are sets of tables & methods grouped by feature, from which SPs are built.

## Slide 23: Template
Base Template
SPInfo
SPTemplates
General Metadata Group
Table and Method Metadata Group
Table
Column
Type
MethodID
AccessControl
SecretProtect
ACE
Authority
Access Control Metadata Group
Certificates
Credential Table Group
C_PIN
C_RSA_1024
C_RSA_2048
C_AES_128
C_EC_160
C_AES_256
C_EC_192
C_EC_224
C_EC_256
C_EC_521
C_EC_163
C_EC_233
C_HMAC_160
C_EC_283
C_HMAC_256
C_HMAC_384
C_HMAC_512
C_EC_384
The Base Template defines a common set of tables and methods, a subset of which SHALL be
incorporated into all SPs.
store an SP’s self-descriptive information, such as SP identification, size, and version numbers.
store data about the tables and methods that make up this SP.
define authorities, the secrets and authentication methods those authorities require, and the access control associations that permit method operation.
define available encryption/decryption algorithms and authentication mechanisms, and also store associated secrets or keys.
enable creation of tables, addition and deletion of rows to tables, and modification of table cell values.
define which authorities are permitted to successfully invoke which methods and modify ACLs
SP Method Group
DeleteSP
Basic Table Method Group
CreateTable
Delete
CreateRow
DeleteRow
Get
Set
Next
GetFreeSpace
GetFreeRow
Method Manipulation Group
DeleteMethod
Access Control Method Group
Authenticate
GetACL
AddACE
RemoveACE
Key Related Method Group
GenKey
GetPackage
SetPackage

## Slide 24: Template
Admin Template
The purpose of the Admin Template is to provide to the Admin SP the capability to optionally issue additional SPs and to maintain information about the TPer.
SPs on the TPer Group
SP
Method
IssueSP
TPer Metadata Group
TPerInfo
Serial Number Contents
CryptoSuite
Tables
Methods

## Slide 25: Template
Clock Template
The Clock Template enables an SP to manage information about time.
ClockTime
Methods
GetClock
SetClockHigh
SetLagHigh
IncrementCounter
ResetClock
SetLagLow
SetClockLow
Tables
Methods
Tern such as :
ExactTime, HighTime, High Trust, IncrementalClock, LagTime, Low Time, Low Trust, MonotonicTime, MonotonicIncrement & Timer Mode

## Slide 26: Template
Crypto Template
The Crypto Template provides a set of cryptographic methods that operate on public and symmetric key store tables, collectively called Credential tables, provided by the Base and other Templates. The Crypto Template also provides a set of tables that supports these methods that enable host invoked cryptographic operations with host-supplied data to occur in the SD.
Cryptographic Support Group
H_SHA_1
H_SHA_256
H_SHA_384
H_SHA_512
Tables
Methods
Method
XOR
Sign
Verify
Decryption Method Group
DecryptInit
DecryptFinalize
Decrypt
Random
Random Number Related Method Group
Stir
Encryption Method Group
EncryptInit
EncryptFinalize
Encrypt
Hash Method Group
HashInit
Hash
HashFinalize
HMAC Method Group
HMACInit
HMAC
HMACFinalize
H_SHA_512

## Slide 27: Template
Locking Template
The Locking Template defines mechanisms for access control to user data (LBA), including controlling media encryption, user data encryption key management, and Read/Write lock state.
Side effects occur when writing cells of the tables of the SP that incorporates the Locking Template. These side effects include enabling Read/Write locking, enabling encryption with a certain encryptionkey, and initiating the re-encryption process.
Tables
LockingInfo
Locking
MBRControl
MBR
K_AES_128
Media Encryption Key Table Group
K_AES_256
Tables

## Slide 28: Template
Log Template
The Log Template is designed to maintain a log of the activities on the SP into which it was issued. The purpose of providing this service is to aid in audits, forensic analysis, and general monitoring of the operation of the SP.
Tables
Methods
Methods
AddLog
CreateLog
ClearLog
FlushLog
Log
Table
LogList

## Slide 29: Access Control
Access control limits the methods that are able to be processed on an SP, a table, or on specific rows and columns of a table.
Access Control setting are configurable and assignable
Permission to process a method is governed by which secrets the method’s invoker has proven that it knows. The secrets and their public parts are called Credentials. The operation for proving knowledge of a secret is called an Authentication Operation.
An authority is used by the host application to represent a person, a role, a program agent, etc. These are distinctions of meaning to the application, not to the SP.

## Slide 30: Access Control
Access Control is specified in layers. The top layer of the mechanism is Access Control Lists (ACLs). ACLs are lists of Access Control Elements (ACEs).
Look up ACLs

## Slide 31: Access Control -- authority
Authentication Credential
Authentication Operation
Required
Credential Table (C_*)
Store authentication secrets

## Slide 32: Access Control -- SP Issuance
Issuance is the cryptographically controlled creation of SPs from templates. Issuance occurs within a session to a TPer's Admin SP, and is achieved by demonstrating knowledge of the secrets required to authorize the creation of new SPs and then, for each new SP, creating a unique credential for the Admin authority on that SP.

## Slide 33: Access Control -- SP Issuance
Every train (SP) must have an engine (Base Template)
Additional cars (other Templates) providing additional capabilities are able to be added at the time of issuance

## Slide 34: Access Control -- Personalization
Personalization follows Issuance.
The Admin each authority on the new SP accomplishes personalization by opening a session to the issued SP, creating new tables (in addition to the tables that were provided by the templates), provisioning those tables, creating and configuring new authorities, and setting the access controls on the SP's methods.
'
'
'

## Slide 35: Access Control – Issuance / Personalization
'
'
'

## Slide 36: Section 3 TCG OPAL

## Slide 37
'